## Slide 1: Network Layer Chapter 5
Responsible for getting packets from the source to destination through INTERMEDIATE HOPS
Data link layer: only between two points
The network layer deals with end to end transmission
  Should know the topology of the network
  Should not overload some routes and underload other routes.
  Should deal with different networks

## Slide 2
The OSI reference model.

## Slide 3: The Network Layer
Application Transport
Responsible for delivering packets between endpoints over multiple
links
Network Link Physical

## Slide 4: Network Layer
Design Issues
Routing Algorithms
Congestion Control
Quality of Service
Internetworking
Network Layer of the Internet

## Slide 5: Design Issues
Store-and-forward packet switching »
Connectionless service – datagrams »
Connection-oriented service – virtual circuits »
Comparison of virtual-circuits and datagrams »

## Slide 6: Store-and-Forward Packet Switching
Components of the network layer
  ISP equipment (routers connected by transmission lines)
  Host H1 is directly connected to one of the router
    Home computer plugged into MODEM
    H2 is a LAN, with an office Internet with a router, F, owned and operated by the customer.
    The router has a leased line to the ISP’s equipment.
    F is not part of ISP, but it runs the same algorithms as the ISP’s routers.
The environment of the network layer protocols.
Host sends the packet to the nearest router, which will be forwarded to the next router along the path until it reaches the destination.

## Slide 7: Services Provided to the Transport Layer
Properties of services
  The services should be independent of router technology
  Transport layer should be shielded from the number, type, and topology of the routers present.
  The network addresses made available to transport layer should use a uniform numbering plan across LANs and WANs.
The freedom resulted into two thoughts
  First: Network service should be connectionless with SEND PACKET and RECEIVE PACKET and little more.
    No ordering and flow control should be done.
    Each packet should carry a destination address.
  Second: network should be reliable and connection-oriented service based on the experience of telephone service.
    Without connections, quality of service is difficult to achieve especially for real-time traffic.
First, connectionless service has dominated.
Later, connection-orient service dominated
Currently, both are widely used.

## Slide 8: Connectionless service: datagrams
Packets are injected as datagrams (analogy is telegram).
No advance setup is needed
Network is called datagram network.
  H1 handover long message to transport layer which instructs to deliver packet to P2 on H2. The transport layer runs in H1 (in the operating system). It prepends transport header and handover it to network layer (another procedure)
Network layer breaks it into packets and sends each of them to router A using point-to-point protocol, PPP.
ISP decided where to send packets. It has to take routing decisions.
The algorithm which does routing decisions are called routing algorithm.
In this chapter, we study routing algorithms.
Internet protocol (IP) is the basis of the Internet, individually forwards each packet. 32 bits in IPv4 and 128 bits in IPv6.

## Slide 9: Connectionless Service – Datagrams
Packet is forwarded using destination address inside it
Different packets may take different paths
Routing within a datagram network.

## Slide 10: Connection-oriented: Virtual Circuits
Idea: Avoid having a new route for every packet.
Establish a connection. When a connection is established, the connection set-up is stored in tables.
  The route is used for all traffic flowing over the connection.
H1 established connection 1 with host H2. The first line of A’s table says that if a pack arrives with connection 1 it should be forwarded to C and given connection id as 1.
If H3 also wants to establish a connection to H2, it choses a connection identifier 1 and tells the network to establish a connection.
There is a conflict as A has already used id 1. So, A assigns a different identifier. This process is called label switching. An example of the protocol is MPLS (MultiProtocol label Switching). It wraps packets with 20-bit connection identifier or label.

## Slide 11: Connection-Oriented – Virtual Circuits
Packet is forwarded along a virtual circuit using tag inside it
Virtual circuit (VC) is set up ahead of time
Routing within a virtual-circuit network.

## Slide 12: Comparison of Virtual-Circuits & Datagrams

## Slide 13: Routing Algorithms (1)
Optimality principle »
Shortest path algorithm »
Flooding »
Distance vector routing »
Link state routing »
Hierarchical routing »
Broadcast routing »
Multicast routing »
Anycast routing »
Routing for mobile hosts »
Routing in ad hoc networks »

## Slide 14: Routing Algorithms
The decision has to be made for every packet as best route may be changed over last time.
Network layer design
  Algorithms and data structures
Routing and forwarding
  Forwarding: a process which takes each packet and forwards it to outgoing line.
  Routing: A process which updates the routing tables.
    Routing algorithms play a major role.
Properties of routing algorithm
  Correctness, simplicity:
  Robustness: it should run for years; hosts fail, routers crash, software fails
  Stability: Routng algorithm should converge and reach equilibrium.
  fairness, efficiency: Difficult to achieve: For example, in case of high traffic between A and A’, B and B’, C and C’, the traffic between X and X’ will be shut off. So compromise is required.

## Slide 15: Routing Algorithms (2)
Routing is the process of discovering network paths
Model the network as a graph of nodes and links
Decide what to optimize (e.g., fairness vs efficiency)
Update routes for changes in topology (e.g., failures)
Forwarding is the sending of packets along a path

## Slide 16: Routing Algorithms
Nonadaptive algorithms
  Decisions do not depend on the state or topology
  When the network is booted, routing tables are fixed.
  Also called static routing algorithms
Adaptive algorithms
  Decisions are based on on the state or topology
  Dynamic routing algorithms

## Slide 17: The Optimality Principle
Each portion of a best path is also a best path; the union of them to a router is a tree called the sink tree
Best means fewest hops in the example
Set of all optimal routes from all sources to a given destination form a sink tree
Goal of routing algorithm: discover and use sink trees for all the routers.
The optimality principle acts as a Benchmark for comparison
(a) A network. (b) A sink tree for router B.

## Slide 18: Shortest Path Algorithm (1)
Dijkstra’s algorithm computes a sink tree on the graph:
Each link is assigned a non-negative weight/distance
Shortest path is the one with lowest total weight
Using weights of 1 gives paths with fewest hops
Algorithm:
Start with sink, set distance at other nodes to infinity
Relax distance to other nodes
Pick the lowest distance node, add it to sink tree
Repeat until all nodes are in the sink tree

## Slide 19: Shortest Path Algorithm (2)
A network and first five steps in computing the shortest paths from A to D. Pink arrows show the sink tree so far.

## Slide 20: Shortest Path Algorithm (3)
. . .
Start with the sink, all other nodes are unreachable
Relaxation step. Lower distance to nodes linked to newest member of the sink tree
. . .

## Slide 21: Shortest Path Algorithm (4)
. . .
Find the lowest distance, add it to the sink tree, and repeat until done

## Slide 22: Flooding
A simple method to send a packet to all network nodes
  Each node floods a new packet received on an incoming link by sending it out all of the other links
Generates vast numbers of duplicate packets.
Method 1:
  Flooding with an hop count: Put hop counter and decrement hop counter for each node.
  -ve: generates exponential number of duplicate pockets
Method 2
  Track the packets. Stop, if it is already flooded, i.e., avoid sending second time.
    Put a sequence number for each source in the packet. Maintain the list at each node.

## Slide 23: Flooding
Flooding is not practical, but has several advantages
  It ensures that packet reaches every node.
  Flooding is tremendously robust.
    Even if large number of routers are damaged, the packet reaches the destination.
  Flooding produces shorter delay
Flooding can be used to compare other algorithms.

## Slide 24: Distance Vector Routing (1)
Dynamic
Distance vector is a distributed routing algorithm
  Shortest path computation is split across nodes
  Each router maintains the table giving the best known distance to each destination
Bellman-Ford Algorithm (followed in ARPANET):
Each node knows the distance of links to its neighbors
Each node advertises vector of lowest known distances to all neighbors
Each node uses received vectors to update its own
Repeat periodically

## Slide 25: Distance Vector Routing (1)
Once every T sec, each router sends to each neighbor a list of estimated delays to the destination. It also receives similar list from its neighbors and calculated the new routing table.
Example
  Four columns show the delay vectors received from neighbors. A claims to have a 12 msec delay to B, 25msec delay to C, and 40 sec delay to D and so on.
  Suppose, J has measured or estimated its delay to its neighbors A, I,H, and K as 8, 10, 12, and 6 respectively.
  J computes time delay to G as follows.
    One route: J,A,..G = 8 (JA) +18 (AG)=26
    Second route: J I ..G=41(31+10)
    Third route: J H..G= 18(6+12)
    Fourth route: JK..G=37 (31+6)
    The best route is 18.

## Slide 26: Distance Vector Routing (2)
(a)A network. (b)Input from A, I, H, K, and the new routing table for J.

## Slide 27: The Count-to-Infinity Problem
Convergence: Though it converges to correct answer, it converges slowly.
Responds rapidly to good news, but very slowly to bad news.
In Figure (a) shows how good news spreads quickly.
Figure (b) demonstrates count to infinity problem.
The count-to-infinity problem.

## Slide 28: Link State Routing (1)
Distance vector routing is replaced by link state routing.
More computation but simpler dynamics
Widely used in the Internet (OSPF, ISIS)
Algorithm: Each router
  Discovers its neighbors and learn their network addresses.
    After booting, node sends HELLO packet to each point-to-point line.
  Set the distance or cost metric to each of its neighbors
  Construct a packet with the learning.
  Send this packet and receive packet from all other routers.
  Compute the shortest path to every other router

## Slide 29: Link State Routing (2) – LSPs
LSP (Link State Packet) for a node lists neighbors and weights of links to reach them
(a) A network. (b) The link state packets for this network.

## Slide 30: Link State Routing (3) – Reliable Flooding
Seq. number and age are used for reliable flooding
New LSPs are acknowledged on the lines they are received and sent on all other lines
Example shows the LSP database at router B
The packet buffer for router B in Fig. 5-12(a).

## Slide 31: Hierarchical Routing
As network grows, the router tables grow proportionately.
  More memory and CPU time
  More bandwidth
After certain limit, it is not possible to send routing table to every other router.
Hierarchical routing
  Routers are divided into regions.
  Each router knows how to route packets to other routers within the region.
  Hierarchy may consists of multiple levels.

## Slide 32: Hierarchical Routing
Hierarchical routing reduces the work of route computation but may result in slightly longer paths than flat routing
Hierarchical routing.

## Slide 33: Broadcast routing
Broadcast sends a packet to all nodes
Simple algorithm: send the packet to each destination.
  It is slow and wastes bandwidth
  Source should have a list of all destinations.
Multi-destination routing
  Each packet contains a list of destinations or a bitmap indicating desired destinations.
  The router generated new copy of the packet for each output line and includes in the packet only those destinations which are on the line.
  After sufficient number of hops the packet will have only one destination
  Bandwidth is used efficiently.

## Slide 34: Broadcast routing
Flooding is another broad cast technique
Reverse path forwarding (figure (c))
When a broadcast packet arrives to the router, the router checks to see if the packet arrived on the link that is normally used for sending packets toward the source of the broadcast.
  If so, there is a chance that broadcast packet might have followed the excellent route.
  The router forward the packet to all links except incoming links.
  If the packet arrives from other link than the preferred one, the pack is discarded as a likely duplicate.
  After 5 hops, with 24 packets broadcasting terminates.
  +ve: easy to implement and efficient; no sequence numbers are required.
Spanning tree algorithm: figure (b)
  Minimum of 14 packets
  -ve: each router should have knowledge of spanning tree

## Slide 35: Broadcast Routing
Broadcast sends a packet to all nodes
RPF (Reverse Path Forwarding): send broadcast received on the link to the source out all remaining links
Alternatively, can build and use sink trees at all nodes
Reverse path forwarding. (a) A network. (b) Sink tree for router I. (c) The tree built by reverse path forwarding from I.

## Slide 36: Multicast Routing (1) – Dense Case
Send a message to well-defined group, numerically large by small than the size of the network
  Example: live video
Multicast sends to a subset of the nodes called a group
Routing algorithm: multicast routing
All multicasting schemes require a way to create and destroy groups and identify which routers are the members of the group.

## Slide 37: Multicast Routing (1) – Dense Case
If the group is dense, employ broadcasting
  Remove those nodes which are not the members in the spanning tree.
  Multicasting spanning tree
    Use link state routing to identify the nodes.
A network. (b) A spanning tree for the leftmost router.
(c) A multicast tree for group 1. (d) A multicast tree for group 2.

## Slide 38: Multicast Routing (2) – Sparse Case
CBT (Core-Based Tree) uses a single tree to multicast
All the members agree on a tree.
Tree is the sink tree from core node to group members
Multicast heads to the core until it reaches the CBT
(a) Core-based tree for group 1. (b) Sending to group 1.

## Slide 39: Anycast Routing
Anycast sends a packet to one (nearest) group member
  Used for time of the day, DNS service
  Falls out of regular routing with a node in many places
(a) Anycast routes to group 1. (b) Topology seen by the routing protocol.

## Slide 40: Routing for Mobile Hosts
Mobile hosts can be reached via a home agent
Fixed home agent tunnels packets to reach the mobile host; reply can optimize path for subsequent packets
No changes to routers or fixed hosts

## Slide 41: Routing in Ad Hoc Networks
The network topology changes as wireless nodes move
Routes are often made on demand.
A’s broadcast reaches B & D
B’s and D’s broadcast reach C, F & G
C’s, F’s and G’s broadcast reach H & I
A’s starts to find route to I

## Slide 42: Congestion Control (1)
Congestion is a situation: Too many packets present in the network causes network delay and loss
Both network and transport layers share the responsibility to control congestion.
Effective way is to reduce the load at the transport layer.
Goodput (=useful packets) trails offered load

## Slide 43: Congestion Control (2)
Network experiences a congestion collapse
If routers will have infinite memory, congestion gets worse
  Packets gets timed out.
Difference between congestion control and flow control
Congestion control is related to whole network. Involves the behavior of all the hosts and routers.
Flow control relates to the traffic between a particular sender and a particular receiver.
Best method is to get host a “slow down”.

## Slide 44: Congestion Control (3) – Approaches
Network must do its best with the offered load
Different approaches at different timescales
Nodes should also reduce offered load (Transport)

## Slide 45: Congestion Control (1)
Handling congestion is the responsibility of the Network and Transport layers working together
− We look at the Network portion here
Traffic-aware routing »
Admission control »
Traffic throttling »
Load shedding »

## Slide 46: Network provisioning
Links and routers that are heavily utilized are upgraded at the earliest opportunity.
  By considering short-term and long-term traffic trends.

## Slide 47: Traffic-Aware Routing
Choose routes depending on traffic, not just topology
Link weight is a function of the link bandwidth, propagation delay, measured load (average queuing delay)
Routing tables are updated accordingly.
E.g., use EI for West-to-East traffic if CF is loaded
-ve: routing tables may oscillate wildly leading to erratic routing and other problems

## Slide 48: Admission Control
Idea: do not set up a new virtual circuit unless the network can carry the added traffic without becoming congested.
  Attempt to set up a virtual circuit may fail.
  Example: telephone system
Issue is handling bursty traffic
  Video is easy to handle
  Traffic due to web browsing is very bursty
Admission control can be combined with traffic ware routing
Redraw the network topology based on information about congested routers.
  For example, normally connection between router A and B passes through one of the congested routers. Based on the information, we can redraw the network.

## Slide 49: Admission Control
Admission control allows a new traffic load only if the network has sufficient capacity, e.g., with virtual circuits
Can combine with looking for an uncongested route
Network with some congested nodes
Uncongested portion and route AB around congestion

## Slide 50: Traffic Throttling
When the congestion is imminent, network should tell the senders to throttle back their transmissions and slow down.
Congestion avoidance
Congested routers signal hosts to slow down traffic for Datagram networks and virtual circuit networks.
Two problems have to be solved for each approach
First: router must determine when congestion is approaching, before it has arrived.
  Queuing delay captures congestion experienced by packets
Second: routers must send timely feedback to the senders that are causing congestion.
  ECN (Explicit Congestion Notification) marks packets and receiver returns signal to sender

## Slide 51: Traffic Throttling: feedback mechanisms
Choke packets
  Router selects the congested packet and sends the choked packet back to source host.
  When a source gets the choked packet, it is supposed to reduced the 50% of traffic.
Explicit congestion notification (ECN)
  The router can tag any packet it forwards to signal that it is experiencing a congestion.
  When a network delivers a packet, the received can inform the sender about congestion through ack. message. The design is called Explicit Congestion Notification (ECN).

## Slide 52: Traffic Throttling: feedback mechanisms
With ECN method, many new packets may be ttransmittted after the congestion.
Alternative approach: Hop-by-Hop Backpressure
  Have the choke packet take effect at every hop it passes through
  Whenever a packet reaches F, F is required to reduce the flow to D.
Example:
  As soon as choke packet reaches F, F is required to reduce the flow to D.
    It gives the D immediate relief
  Similarly when a choke packet reaches E, E has to reduce the flow to F.
(a) A choke packet that affects only the source. (b) A choke packet that affects each hop it passes through.

## Slide 53: Load Shedding (1)
When all else fails, network will drop packets (shed load)
When routers are being inundated by packets that they can not handle, they just throw them away.
Key question
  Which packets to drop?
  File transfer: old packet is important
    WINE policy
  Realtime traffic: new packet is important
    MILK policy
Application must mark the importance on the packets.
Random Early Detection
  Routers maintain running average of queue length
  When a queue length exceeds, router starts dropping the packets at random.
  Send will notice the loss as there are no ack. And slow down
  Better performance.

## Slide 54: Load Shedding (1)
Random Early Detection
  Routers maintain running average of queue length
  When an average queue length exceeds, router starts dropping the packets at random.
    Fast senders will have more packet drop
  Sender will notice the loss as there are no ack. and slow down
  Better performance.

## Slide 55: Quality of Service
So far, we have made effort to improve network performance
However, some applications require stronger performance guarantees.
  Example: Multimedia applications:
We will focus of providing network performance with a sharp focus on providing quality of service.
One solution is overprovisioning
  More money is required
With quality of service mechanisms, the network can honor performance guarantees at the cost of turning down some requests.
Issues
  What applications need from the network?
  How to regulate the traffic that enters the network?
  How to reserve the resources at routers to guarantee performance?
  Whether the network can safely accept more traffic
No single technique deals efficiently all these issues..

## Slide 56: Quality of Service
Application requirements »
Traffic shaping »
Packet scheduling »
Admission control »
Integrated services »
Differentiated services »

## Slide 57: Parameters Defining QoS
Throughput/bandwidth - the total amount of work completed during a specific time interval.
Delay - the elapsed time from when a request is first submitted to and when the desired result is produced.
Jitter - the delays that occur during the playback of a stream.
  Due to lost frames.
  Not acceptable for continuous media applications
  Random variation of transmission time
Reliability/loss - how errors are handled during transmission and processing of continuous media.

## Slide 58: Application Requirements (1)
Different applications care about different properties
We want all applications to get what they need
.
Stringency of applications' quality-of-service requirements.
Application | Bandwidth | Delay | Jitter | Loss
Email | Low | Low | Low | Medium
File sharing | High | Low | Low | Medium
Web access | Medium | Medium | Low | Medium
Remote login | Low | Medium | Medium | Medium
Audio on demand | Low | Low | High | Low
Video on demand | High | Low | High | Low
Telephony | Low | High | High | Low
Videoconferencing | High | High | High | Low

## Slide 59: Application Requirements (2)
Bandwidth:
  E-mail, audio, remote login not need much bandwidth. But file sharing and video in all forms need high bandwidth.
Delay:
  File transfer, email, audio, and video are not delay sensitive. That is if the packets are delayed uniformly across all by a few seconds, no harm is done. So, playing audio or video files from a server does not require low delay.
  But, interactive applications, web access surfing and remote login are more delay sensitive. Telephony, and video conferencing are strictly delay sensitive
.
Jitter
  E-mail, file sharing and web access not sensitive to irregular arrival of packets.
  Remote login is sensitive
  Video and audio are extremely sensitive to Jitter
Loss:
  E-mail, file sharing, web access and remote login have more stringent requirements on loss and bits should be delivered correctly.
  Audio and video applications tolerate lost packets.
    People do not notice short pauses or skipped frames.

## Slide 60: Application Requirements (3)
Network support different categories of QoS
  Constant bit rate (telephony)
    Simulate a wire by providing uniform bandwidth and a uniform delay
  Real-time variable bit rate (e.g., compressed video conferencing)
    Sending a complex frame requires many bits, where a shot of white ball requires less bits.
  Non-real-time variable bit rate (e.g., watching a movie on demand)
    Buffering can be used
  Available bit rate (e.g., file transfer)
    -Use the available bandwidth.
.

## Slide 61: Application Requirements (2)
Network provides service with different kinds of QoS (Quality of Service) to meet application requirements
Network Service | Application
Constant bit rate | Telephony
Real-time variable bit rate | Videoconferencing
Non-real-time variable bit rate | Streaming a movie
Available bit rate | File transfer
Example of QoS categories from ATM networks

## Slide 62: Traffic Shaping (1)
We must know that traffic is being guaranteed
However, traffic in data is BURSTY!
Bursts in the traffic are difficult to handle than constant rate traffic as they can fill the buffers and cause packets to be lost.
Traffic shaping
  regulates the average rate and burstiness
Monitoring traffic flow is called “Traffic policing”
Traffic shaping and Traffic policing are important for real-time data (audio and video).

## Slide 63: Leaky bucket algorithm
Sliding window controls the data to be transmitted.
Leaky bucket algorithm
  Imagine a bucket with a small hole at the bottom.
  No matter the rate the data enters, the outflow is constant.
  Once the bucket is full with a capacity B, any additional water splits over the sides and lost.
  Algorithm
    Each host is connected to the network containing a leaky bucket.
    If the packet arrives when the bucket is full, it is queued until enough water leaks out to hold it or be discarded.

## Slide 64: Leaky and Token buckets
(a) Shaping packets. (b) A leaky bucket. (c) A token bucket.

## Slide 65: Token bucket algorithm
Imagine a bucket that is being filled. A tap is running at the rate R and the bucket has a capacity of B, as before.
To send a packet, we must able to take water or tokens as out of bucket.
If the bucket is empty, we must wait till tokens arrive.
No more than a fixed number of tokens can accumulate in the bucket.
Both leaky and token bucket algorithms smoothen the traffic by limiting the rate of flow.

## Slide 66: Traffic Shaping (3)
(a) Traffic from a host. Output shaped by a token bucket of rate 200 Mbps and capacity (b) 9600 KB and (c) 0 KB. Token bucket level for shaping with rate 200 Mbps and capacity (d) 16,000 KB, (e) 9600 KB, and (f) 0 KB.
Both leaky and token bucket algorithms smoothen the traffic by limiting the rate of flow.

## Slide 67
Host generates the traffic pattern as shown in Figure (a). The pattern in bursty.
  Average rate over one second is 200Mbps, even though the host sends a burst of 16,000 KB at the top speed of 1000 Mbps (1/8 of second).
  Routers can only accept data until only the buffers are filled. The buffer size is 9600 KB, smaller than the traffic burst. Some of the packets will be dropped.
With token bucket, we can shape the traffic. The output of token bucket is shown in Figure (b). The host can send full throttle for a short while, until it has drained the bucket. It will cut back 200Mbps until the burst has been sent.
The level of token bucket is given in Figure (e)
We can also shape the traffic to be less busty. Figure (c) shows the output of a token bucket with R=200 Mbps and a capacity of zero. This is the extreme case. The corresponding bucket level Figure (f) is always empty.
Figure (d) shows the bucket level for a token bucket with R=200 Mbps and a capacity of B=16,000 KB.
This is the smallest token bucket through which the traffic passes unaltered.
Leaky and token buckets are easy to implement.

## Slide 68: Packet Scheduling (1)
Regulating the traffic is OK.
However, to provide performance guarantee, we must reserve sufficient resources along the route for performance guarantee.
Packet scheduling algorithms
  Allocate router resources among the packets of a flow and between competing flows.
Three kinds of resources are reserved
  Bandwidth
    If flow requires 1Mbps and bandwidth is 2Mbps, one should not try to get three flows through a line.
  Buffer space
    Purpose of buffer is to absorb the small bursts. To have quality of service, some buffers are reserved for a specific flow.
  CPU cycles
    Making sure that CPU is not loaded

## Slide 69: Packet Scheduling (1)
FIFO: First-Come-First-Serve
  Drop newly arrived packets
  Tail drop behavior
  Simple to implement
  Not good for achieving quality of service in case of multiple flows
Fair queuing round-robin
  Routers have separate queues, one for each flow.
  When line becomes idle, the router scans queues in a round robin fashion.
Round-robin fair queueing.

## Slide 70: Packet Scheduling (2)
Byte-byte round robin.
  Compute the virtual time that is the number of round at which each packet would finish being sent.
  It gives all hosts the same priority
Weighted Fair Scheduling (WFG)
  Number of bytes per round will be weight (W) of the flow.
  Fi=max(Ai,Fi-1)+Li/W
    Ai is the arrival time, Fi is the finish time, Li is the length of the packet
(a) Weighted Fair Queueing. (b) Finishing times for the packets.

## Slide 71: Admission Control (1)
Admission control takes a traffic flow specification and decides whether the network can carry it
Sets up packet scheduling to meet QoS
Example flow specification

## Slide 72: Admission Control (2)
Construction to guarantee bandwidth B and delay D:
Shape traffic source to a (R, B) token bucket
Run WFQ (Waited Fair Queue) with weight W / all weights > R/capacity
Holds for all traffic patterns, all topologies

## Slide 73: Network Layer in the Internet (1)
IP Version 4 »
IP Addresses »
IP Version 6 »
Internet Control Protocols »
Label Switching and MPLS »
OSPF—An Interior Gateway Routing Protocol »
BGP—The Exterior Gateway Routing Protocol »
Internet Multicasting »
Mobile IP »

## Slide 74: Network Layer in the Internet (2)
IP has been shaped by guiding principles:
Make sure it works
Keep it simple
Make clear choices
Exploit modularity
Expect heterogeneity
Avoid static options and parameters
Look for good design (not perfect)
Strict sending, tolerant receiving
Think about scalability
Consider performance and cost

## Slide 75
Network Layer in the Internet (3)
Internet is an interconnected collection of many networks that is held together by the IP protocol

## Slide 76
IP Version 4 Protocol (1)
IPv4 (Internet Protocol) header is carried on all packets and has fields for the key parts of the protocol:

## Slide 77
IP Version 4 Protocol (1)
Version filed
IHL: header length
Differentiated services: type of service
Total length: every thing in the datagram
Identification field: which packet the newly arrived fragment belong to
  All the fragments of the same packet have the same identification code.
Next field: not defined
DF: do not fragment
MF more fragments
  It is set to know whether all the fragments of datagram have arrived.
Fragment offset
  Where in the current packet this packet belongs
TtL: Time to live
  To limit packet life time
  Decremented after each hop
Protocol: UDP or TCP
Header checksum
Source and destination address indicate the IP address of source and destination
Options field
  For other ideas
  Security
  Strict route
    Set of routes
  Lose routes
    Set of routes

## Slide 78: IP Addresses (1) – Prefixes
Addresses are allocated in blocks called prefixes
Prefix is determined by the network portion
Has 2L addresses aligned on 2L boundary
Written address/length, e.g., 18.0.31.0/24

## Slide 79: IP Addresses (2) – Subnets
Subnetting splits up IP prefix to help with management
Looks like a single prefix outside the network
ISP gives network a single prefix
Network divides it into subnets internally

## Slide 80: IP Addresses (3) – Aggregation
Aggregation joins multiple IP prefixes into a single larger prefix to reduce routing table size
ISP advertises
a single prefix
ISP customers have different prefixes

## Slide 81: IP Addresses (5) – Classful Addresing
Old addresses came in blocks of fixed size (A, B, C)
Carries size as part of address, but lacks flexibility
Called classful (vs. classless) addressing

## Slide 82: IP Addresses (6) – NAT
NAT (Network Address Translation) box maps one external IP address to many internal IP addresses
Uses TCP/UDP port to tell connections apart
Violates layering; very common in homes, etc.

## Slide 83: Internet Control Protocols (1)
IP works with the help of several control protocols:
ICMP is a companion to IP that returns error info
  Required, and used in many ways, e.g., for traceroute
ARP finds Ethernet address of a local IP address
  Glue that is needed to send any IP packets
  Host queries an address and the owner replies
DHCP assigns a local IP address to a host
  Gets host started by automatically configuring it
  Host sends request to server, which grants a lease

## Slide 84
Internet Control Protocols (2)
Main ICMP (Internet Control Message Protocol) types:

## Slide 85
Internet Control Protocols (3)
ARP (Address Resolution Protocol) lets nodes find target Ethernet addresses [pink] from their IP addresses

## Slide 86: Label Switching and MPLS (1)
MPLS (Multi-Protocol Label Switching) sends packets along established paths; ISPs can use for QoS
Path indicated with label below the IP layer

## Slide 87: Chapter 5
End